## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 2: Number Systems

## Slide 2: Corrections
No partial credit for either submission of assignments

## Slide 3: Announcements
Discord server for this course – see Syllabus
Labs start this week
First homework due next Wednesday
When HW is posted
Makeup and resubmission lab
  Thursdays 1-5pm

## Slide 4: To the Experts here
“What were we put here to do if not help each other through?” -Mark Horstman

## Slide 5: Outline
Number representations (number systems)
Conversions+

## Slide 6: Decimal
The system you are used to
  There are 10 digits (0 [the first] to 9 [the tenth])
When you use all the digits, a new digit goes in the next position up
42 = (4 x 10) + (2 x 1)
The new position has added weight

## Slide 7: Decimal
Each digit to the left has increasing weight
105 104 103 102 101 100
Weights continue to work after a decimal point
102 101 100 . 10-1 10-2 10-3

## Slide 8: Example
851.96
(8 x 102) + (5 x 101) + (1 x 100) + (9 x 10-1) + (6 x 10-2)
(8 x 100) + (5 x 10) + (1 x 1) + (9 x 0.1) + (6 x 0.01)
+ 50 + 1 + 0.9 + 0.06
The weight on the 6 is 0.01 (or 1/100)

## Slide 9: Decimal
Power of 10 | Decimal
100 | 1
101 | 10
102 | 100
103 | Thousand or Kilo
106 | Million or Mega
109 | Billion or Giga
1012 | Trillion or Tera
Power of 10 | Decimal
10-1 | Tenth
10-2 | Hundredth
10-3 | Thousandth or Milli
10-6 | Micro
10-9 | Nano
10-12 | Pico

## Slide 10: Binary
Same a decimal, but there are only 2 digits (bits)
0 then 1 then 10 then 11 then 100
Weight increases with each digit to the left
  The base is different (2 instead of 10)
100 = (1 x 22) + (0 x 21) + (0 x 20)
= (1 x 4) + (0 x 2) + (0 x 1)
= 4

## Slide 11: MSB and LSB
Left most bit = Most significant bit
Rightmost bit = Least significant bit
1010
MSB LSB

## Slide 12: Binary
Weights can continue after binary point
  We usually don’t use it
Binary | Decimal
2-1 | 1/2 or 0.5
2-2 | 1/4 or 0.25
2-3 | 1/8 or 0.125

## Slide 13: Binary and Decimal
Decimal | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
Decimal | Binary
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111

## Slide 14: Powers of 2
Power of 2 | Decimal
20 | 1
21 | 2
22 | 4
23 | 8
24 | 16
25 | 32
26 | 64
Power of 2 | Decimal
27 | 128
28 | 256
29 | 512
210 | 1,024 = 1k
220 | 1,048,576 = 1M
230 | 1,073,741,824 = 1G
240 | 1T

## Slide 15: Bits needed
How many bits to represent a decimal number?
Largest decimal number = 2n – 1
  Need to include zero
  How many bits is n
22 – 1 = 3
23 – 1 = 7
24 – 1 = 15

## Slide 16: Octal
Base 8 number system
  Not used a lot these days
  chmod command
Decimal | Octal
0 | 0
1 | 1
2 | 2
3 | 3
4 | 4
5 | 5
6 | 6
7 | 7
8 | 10
9 | 11

## Slide 17: Hexadecimal
Base 16 Number System
Need extra digits that aren’t in decimal system
Decimal | Hex
9 | 9
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F
16 | 10
17 | 11
Decimal | Hex
0 | 0
1 | 1
2 | 2
3 | 3
4 | 4
5 | 5
6 | 6
7 | 7
8 | 8

## Slide 18: Converions
Binary, Octal, Hex, and Decimal
1011001111102=54768=B3E16=287810
also
0b101100111110=0o5476=0xB3E=2878

## Slide 19: Binary to Octal/Hex and vice versa
Easiest
Hex is a grouping of 4 bits (24 = 16)
Octal is a grouping of 3 bits (23 = 8)

## Slide 20: Example
1011001111102 = 101 100 111 110
= 5 4 7 6
= 54768
1011001111102 = 1011 0011 1110
= B 3 E
= B3E16

## Slide 21: Example
A4916 = A 4 9
= 1010 0100 1001
= 1010010010012
7138 = 7 1 3
= 111 001 011
= 1110010112

## Slide 22: Binary to Decimal
Use your powers of 2 and add
110010102 -7 bits
2726252423222120
1 1 0 0 1 0 1 0
27+26+23+21
128+64+8+2 = 202

## Slide 23: Decimal to Binary
Sum of Weights Method
  Use largest weight that is smaller than you #, then subtract and repeat until zero is left
102 next smallest weight is 64=26
102-64=38 next smallest weight is 32=25
38-32=6 next smallest weight is 4=22
6-4=2 next smallest weight is 2=21
2-2=0 DONE
102=26252221=11001102

## Slide 24: Decimal to Binary
Divide by 2 Method
  Divide number by 2 repeatedly (whole #s and remainders until zero is left)
102/2=51 even # to start, so no remainder = 0
51/2=25 odd # to start, so remainder = 1
25/2=12 odd # to start, so remainder = 1
12/2=6 even # to start, so no remainder = 0
6/2=3 even # to start, so no remainder = 0
3/2=1 odd # to start, so remainder = 1
1/2=0 odd # to start, so remainder = 1 DONE
Put the numbers together backwards (first division was LSB, last one was MSB)
102 = 11001102

## Slide 25: Decimal to Octal/Hex and vice versa
Decimal -> Binary -> Octal/Hex
Octal/Hex -> Binary -> Decimal
You already know all of these steps

## Slide 26: Reading
This lecture
  Sections 2.1-2.3, 2.8-2.9
Next lecture
  Sections 2.4-2.7