## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 3: Arithmetic and Complements

## Slide 2: Binary Arithmetic
By hand, it uses all the same rules you know for decimal arithmetic

## Slide 3: Binary Addition
4 Rules
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10 The sum is 0 and the carry is 1

## Slide 4: Binary Addition
Carry is the same as for decimal
19 119 Put carry here
+ 1 + 1
0 First col adds to 10 20

## Slide 5: Binary Addition Examples
100 + 110
010 + 1
11 + 111
011.1 + 111.01

## Slide 6: Binary Multiplication
Easiest multiplication table ever!
0 x 0 = 0
0 x 1 = 0
1 x 0 = 0
1 x 1 = 1

## Slide 7: Binary Multiplication
Makes partial products a breeze
100 11.1
x110 x 11
000 111
100 +111
+100 1010.1
11000

## Slide 8: Binary Subtraction
The usual rules for positive numbers where you subtract a smaller number from a bigger number
Subtract each column and do a borrow, if necessary

## Slide 9: Binary Subtraction
11000 1010
- 100 - 111
10100 0011

## Slide 10: Binary Subtraction
The rules work well for a small subset of arithmetic problems
  What about negative numbers?
  What about subtracting a larger # from a smaller one?
Complements!

## Slide 11: Binary Division
Just like decimal, same as the other operators

## Slide 12: Unsigned Numbers
The number of bits n used to store the # determine the max value, 2n - 1
For 4 bits, max value = 24 = 15
  Not 16 because of including zero
For 8 bits, max value = 255
For 16 bits, max value = 65,535

## Slide 13: Complements
Used to express or store negative numbers
Turns subtraction into addition, which is easier
In general, there are 2 types of complements
  Diminished radix complement (1’s complement)
  Radix complement (2’s complement)

## Slide 14: 1’s Complement
Invert every bit (1 to 0, 0 to 1)
  Keep the same number of bits
11000
00111

## Slide 15: 2’s Complement
Take a 1’s Complement of a # and add 1
2’s Complement = (1’s Complement) + 1
11000
00111
+ 1
01000

## Slide 16: 2’s Complment
Another way to get it is to start at the LSB and move left
When you get to the first 1, invert all bits to the left of it
Invert 11000 No inversion
01000

## Slide 17: 2’s Complement Examples
111
10101
10111
100

## Slide 18: 9’s and 10’s Complement
Like 1’s and 2’s Complement, but for decimal
  Feel free to look at it
  Not used in this class

## Slide 19: Signed Numbers
Splits the value range for neg and pos #’s
  Max value = 2n-1 - 1
  Min value = -(2n)
For 4 bits, -8 to 7
For 8 bits, max value = -128 to 127
For 16 bits, max value = -32,768 to 32,767

## Slide 20: Signed Numbers
Highest bit (MSB) is a sign bit
  0 is positive
  1 is negative
Negative #’s are the 2’s complement of the equivalent positive #
-1 = 1 = 0000 0001 = 1111 1110 = 1111 1111 = -1
Pos # 1’s Comp 2’s Comp

## Slide 21: Signed Numbers
Weights are slightly modified
  MSB is negative
27 26 25 24 23 22 21 20 for unsigned becomes
-27 26 25 24 23 22 21 20 for signed
1011 is -23 + 21 + 20 = -8 + 2 + 1 = -5
1111 is -23 + 22 + 21 + 20 = -8 + 4 + 2 + 1 = -1

## Slide 22: Signed Number Addition
Pad with leading zeros to fill the bit size
Add the two numbers
Throw away carry
0000 1111 15 0100 1010 74
+1111 0001 +(-15) +1000 1111 +(-113)
1 0000 0000 0 1101 1001 -39

## Slide 23: Signed Number Subtraction
Take the 2’s complement of the 2nd #, then add
0000 1111 15 0100 1010 74
- 0000 1111 -15 - 0111 0001 -113
0000 0000 0 1101 1001 -39

## Slide 24: Reading
This lecture
  Sections 2.4-2.7
Next lecture
  Sections 2.10-2.12