## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 7: PLDs, Boolean Laws, and Equipment

## Slide 2: PLDs

## Slide 3: OTPs
One Time Programmable
Many types
Burn it out!

## Slide 4: Reprogrammable
Different tech
Different cost
  More circuitry

## Slide 5: ROM/RAM
Same concept as PLD
Address lines in
Stores data
RAM vs ROM

## Slide 6: Programming

## Slide 7: Programming/Debugging
Development
In-system
  JTAG
  SWD

## Slide 8: Boolean Addition
Same as OR
  Remember that here 0=FALSE, 1=TRUE

## Slide 9: Boolean Multiplication
Same as AND

## Slide 10: Boolean Laws
Commutative Laws
Associative Laws
Distributive Laws
12 Rules for Simplification
Why?
  Not every system has these laws, i.e. matrices

## Slide 11: Commutative Laws
A + B = B + A
AB = BA

## Slide 12: Associative Laws
A + (B + C) = (A + B) + C
A(BC) = (AB)C

## Slide 13: Distributive Laws
A(B + C) = AB + AC

## Slide 14: 12 Rules for Simplification
1. A + 0 = A
2. A + 1 = 1

## Slide 15: 12 Rules for Simplification
3. A ∙ 0 = 0
4. A ∙ 1 = A

## Slide 16: 12 Rules for Simplification
5. A + A = A
6. A + A’ = 1

## Slide 17: 12 Rules for Simplification
7. A ∙ A = A
8. A ∙ A’ = 0

## Slide 18: 12 Rules for Simplification
9. A’’ = A
10. A + AB = A

## Slide 19: 12 Rules for Simplification
11. A + A’B = A + B
12. (A + B)(A + C) = A + BC
  Also follows from distribution, Rule 7, and Rule 10
  Diagram in book

## Slide 20: Equipment
Test and debugging equipment
Debugging origin
  Literal bugs

## Slide 21: Multimeter
Your best friend!
  Voltage
  Current
  Resistance
  Continuity

## Slide 22: Oscilloscope
Oscope or scope
  Measures and displays signals
The fastest ADC you’ll typically use

## Slide 23: Oscope

## Slide 24: Oscope
Vertical and Horizontal controls
Triggers

## Slide 25: Oscope
AC vs DC coupling

## Slide 26: Oscope
Compensation and Loading
Shopping cart example

## Slide 27: Probes
Voltage
Current
Multi

## Slide 28: Power Supply
DC Voltages
  Circuit power
  Very stable

## Slide 29: Generators
Arbitrary vs Function

## Slide 30: Logic Analyzer
Oscope+
Can measure
  And decode!
Costs extra

## Slide 31: Others
Frequency Analyzer
RLC meters
Fiber optics
Anything you could want, pretty much

## Slide 32: Reading
This lecture
  Sections 3.7, 1.7, 4.1-4.2
Next lecture
  Sections 4.3-4.6