## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 8: DeMorgan’s and Boolean Simplification

## Slide 2: Mastery
First submission
  You can get between 0% and 100% for HW total
  Correct problems – full credit, no change on resubmission
  Incorrect problems – no credit, can be corrected in resubmission
Second submission
  Submit corrected work
  Must include a reflection to change a 0% to 100%
    Why did you get it wrong the first time and what did you learn to correct the error
    Full sentences

## Slide 3: Test
Next Wednesday – 02/23
In class
Turn in paper submissions
All material through this week is fair game
1 handwritten cheat sheet, both sides
Calculator

## Slide 4: NAND and NOR Equivalents
Foreshadowing…

## Slide 5: DeMorgan’s Theorem
The mathematical equivalent
(XY)’ = X’ + Y’
(X + Y)’ = X’Y’

## Slide 6: Examples
(XYZ)’
(X’ + Y’ + Z’)’
(W’X + Y’Z’)’
((A’ + B’) + C’)’
(A’B(C + D’) + E)’

## Slide 7: DeMorgan’s and XOR
Substitution required
B = AB’ + A’B
Using the Laws and 12 Rules:
XNOR = ( B)’ = A’B’ + AB

## Slide 8: Analysis of Circuits
Start at the left and work right
  (Beginning to end of circuit)
Carry a logical output forward as an input

## Slide 9: Analysis of Circuits
Make a truth table
  2 ^ #inputs is how many rows there are
A | B | C | D | CD | B+CD | A(B+CD)
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 0
A | B | C | D | CD | B+CD | A(B+CD)
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 10: Simplification
Boolean Algebra
Karnaugh Maps

## Slide 11: Boolean Algebra
Simplify expressions using the laws and 12 rules
  Group terms together that have common terms
  Simplify negations using DeMorgan’s
  Remove un-needed terms using the rules
    A + 0 = A, A ∙ 1 = A, etc.

## Slide 12: Examples
A’BC + AB’C’ + A’B’C’ + AB’C + ABC
(AB)’ + (AC)’ + A’B’C’
A + AB + AB’C

## Slide 13: Standard Forms
Sum-of-products (SOP)
Product-of-sums (POS)
Standard forms makes things easier

## Slide 14: SOP
All terms have + or ∙ between them and no ()
AB + AC + ABC
A’B + AC + A’B’C’
A(B + C) + AB
(AB)’ + AC

## Slide 15: Making SOP
Distribute and DeMorgan’s
A(B + C) + AB = AB + AC
(AB)’ + AC = A’ + B’ + AC

## Slide 16: Standard SOP
All inputs need to be in each product term
A’BC + AB’C + A’B’C
ABC + AB + A’BC’

## Slide 17: Expanding SOP to Standard SOP
Use Rule 6: A + A’ = 1
Multiply terms by the missing variable using Rule 6 and expand
A’BC + AB + A’BC’
AB(C + C’) = ABC + ABC’
A’BC + ABC + ABC’ + A’BC’

## Slide 18: Why?
Each term in the final expression is a line in the truth table for a 1
You could read the truth table from the expression
A’BC + ABC + ABC’ + A’BC’ = 0’11 + 111 + 110’ + 0’10’

## Slide 19: Example
AB + AB’CD
Expand twice

## Slide 20: POS
All terms are groupings of +, multiplied together
Not can only apply to one input term at a time
(A’ + B)(A + B + C’)(A)
(A + B)’(AB + C)

## Slide 21: Making POS
Use DeMorgan’s and Rule 12: (A + B)(A + C) = A + BC
(A + B)’ = A’B’ = (A’)(B’)
(AB + C) = (A + C)(B + C)

## Slide 22: Standard POS
All inputs need to be in each sum term
(A’ + B + C)(A + B’ + C)(A’ + B’ + C)
(A + B + C)(A + B)(A’ + B + C’)

## Slide 23: Expanding POS to Standard POS
Use Rule 8: A ∙ A’ = 0 to add terms
Expand using Rule 12
(A’ + B + C)(A + B)(A’ + B + C’)
(A + B + CC’) = (A + B + C)(A + B + C’)
(A’ + B + C) (A + B + C)(A + B + C’)(A’ + B + C’)

## Slide 24: Why?
Each term in the final expression is a line in the truth table for a 0
You could read the truth table from the expression
(A’ + B + C) (A + B + C)(A + B + C’)(A’ + B + C’) = (1’+0+0)(0+0+0)(0+0+1’)(1’+0+1’)

## Slide 25: Example
(A + B)(A + B’ + C + D)
Expand twice

## Slide 26: Reading
This lecture
  Sections 4.3-4.6
Next lecture
  Sections 4.7-4.10