## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 5: Logic Gates and Boolean

## Slide 2: Binary Storage
Binary cell
  Stores 1 bit
Register
  A group of n cells, stores a value from 0 to 2n – 1
  Encoding scheme matters

## Slide 3: Example
Keyboard to Memory
  Not USB here
  Probably PS/2 using ACSII

## Slide 4: Binary Processing
There are large blocks in a uC
  Specialized functions
10 bit adder here
Need to go deeper

## Slide 5: Electrical Review
Voltage: Difference in electric potential between two points
  Analogous to water pressure
Current: Flow of charge
  Analogous to water flow
Resistance: Tendency of wire to resist current flow
  Analogous to water pipe diameter
V = I x R (Ohm’s Law)

## Slide 6: Representing Binary with Voltage
Logic Levels

## Slide 7: Why the Voltage Ranges?
Resistance
Capacitance
Transmission
Noise
Floating Ground
Speed

## Slide 8: Switches
3 parts
  Source input
  Output
  Control input
Manual switches?! No!
Timeline:
  1930s – Relays
  1940s – Vacuum Tubes
  1950s – Discrete transistors
  1960s Integrated Circuits (ICs)
    From a few, to tens, to hundreds, to billions today

## Slide 9: Transistors
Two Types – BJT and MOSFET
  Bipolar Junction Transistor
  Metal-Oxide-Semiconductor Field-Effect Transistor

## Slide 10: Example
CMOS Inverter
  Inverts the input
  Input 1 makes output 0
  Input 0 makes output 1

## Slide 11: Boolean Logic Gates

## Slide 12: Boolean Algebra
Variable – symbol to represent action, condition, or data
Complement – inverse of a variable
Literal – variable or complement
Basic Operators – AND, OR, NOT

## Slide 13: Boolean in History
Developed mid-1800’s by George Boole to formalize human thought and logic (also in PHIL114)
  “I’ll go to lunch if Mary goes or John goes, and Sally does not go”
    Let F represent my going to lunch (1 means I go, 0 I don’t go)
    Likewise, m for Mary going, j for John, and s for Sally
    Then F = (m OR j) AND NOT(s)
You can formally evaluate the statement
  m=1, j=0, s=1 then F = (1 OR 0) AND NOT(1) = 1 AND 0 = 0
You can formally transform the statement (covered later)
  F = (m AND NOT(s)) OR (j AND NOT(s))
  Same outputs

## Slide 14: Evaluation
F = (a AND b) OR (c AND d)
  a=1, b=1, c=1, d=0
    F = (1 AND 1) OR (1 AND 0) = 1 OR 0 = 1
  a=0, b=1, c=0, d=1
    F = (0 AND 1) OR (0 AND 1) = 0 OR 0 = 0
  a=1, b=1, c=1, d=1
    F = (1 AND 1) OR (1 AND 1) = 1 OR 1 = 1

## Slide 15: English to Boolean
Pick variables (things that can be represented in 2 different states
Look at the logic words – both, either, and, etc
Construct a Boolean statement

## Slide 16: Examples
F is true if
  a is 1 and b is 1
    F = a AND b
  Either a or b is 1
    F = a OR b
  a is 1 and b is 0
    F = a AND NOT(b)

## Slide 17: Example
A fire sprinkler should spray water is high heat is sensed and the system is set to enabled
  Let h represent “high heat is sensed”
  Let e represent “enabled”
  Let F represent “spraying water”
  Then F = h AND e

## Slide 18: Example
A car alarm should sound if the alarm is enabled, and either the car is shaken or the door is opened
  Let a represent alarm is enabled, s represent car is shaken, d represent door is opened, and F represent alarm sounds
    Then F= a AND (s OR d)
  Alternatively, let d represent that the door is closed (so 1=closed, 0=open)
    Then F = a AND (s OR NOT(d))

## Slide 19: AND/OR/NOT Logic Gates

## Slide 20: Multiple Inputs
Multiple input AND
  Returns 1 when all the inputs are 1
  Returns 0 when at least one input is 0
Multiple input OR
  Returns 1 when at least one input is 1
  Returns 0 when all the inputs are 0

## Slide 21: Example
Problem: The seatbelt light should turn on if the key is in the ignition, the person is in the seat, and the seat belt has not been fastened
Variables:
  S = 1: seatbelt is fastened
  K = 1: key is in the ignition
  P = 1: person is in the seat
Equation
  F = K AND P AND NOT(S)
Circuit

## Slide 22: Boolean Notation (Shorthand)
To not write AND, OR, NOT all the time
  AND becomes multiplication
  OR becomes addition
  NOT becomes apostrophe (X’)or bar (X)
F = (A AND B) OR C → F = AB + C
F = (A AND NOT(B) OR C → F = AB’ + C
F = NOT(A) AND NOT(B) → F = A’B’

## Slide 23: Boolean Equation to Circuit
F = (AB)’ + C + (D + EF)’

## Slide 24: Reading
This lecture
  Sections 3.1-3.3
Next lecture
  Sections 3.4-3.6, 1.6